Line Following Robot with PID Control (Arduino Uno)
Functionality
This project implements a high-performance line following robot using an Arduino Uno and a PID controller. The robot follows a black line on a white surface using 8 IR sensors for precise position tracking. The key highlights of this robot include:
- Real-time PID control for accurate line tracking, especially around sharp 90° turns.
- Dynamic speed adjustment based on the amount of error to prevent overshooting.
- Robust handling of corner cases like full line loss or end-of-track detection.
- Visual status indicators using onboard LEDs.
- Failsafe conditions to stop the robot in case of complete line loss or end-zone detection.
The robot continuously reads the IR sensors, calculates the line's position relative to the center, and adjusts the left and right motor speeds using PID to keep the robot centered on the line. It also includes timers to detect:
- When the robot has lost the line for more than 500 milliseconds.
- When the robot enters an end zone (all sensors detect white) for more than 1 second.

Components Used
Component	Quantity	Description
Arduino Uno	1	Microcontroller board for main processing
IR Sensor Array	8	Digital IR reflective sensors for line detection
L298N Motor Driver	1	Dual H-bridge driver to control the DC motors
DC Gear Motors	2	Motors for left and right wheels
Wheels	2	Attached to the motors
Chassis	1	Platform to mount all components
Power Supply	1	Battery pack (typically 7.4V Li-ion or 9V for field use)
Jumper Wires	-	For making all the necessary electrical connections
White LED	1	Indicates robot is active
Red LED	1	Indicates robot has stopped (end or error)

Connections
Motor Driver (L298N) to Arduino Uno
L298N Pin	Arduino Uno Pin
AIN1	A1
AIN2	A2
BIN1	A3
BIN2	A4
PWMA	D10
PWMB	D11
STBY	A0

IR Sensors (Digital)
IR Sensor	Arduino Pin
IR1	D2
IR2	D3
IR3	D4
IR4	D5
IR5	D6
IR6	D7
IR7	D8
IR8	D9

LED Indicators
LED	Arduino Pin
White LED	D12
Red LED	D13

PID Control Explanation
PID stands for Proportional, Integral, and Derivative — a feedback control algorithm used here to adjust motor speeds for precise line tracking. Here’s how each part contributes:
1. Proportional (P):
  1. Calculates error = (current position - center position)
  2. The greater the error, the stronger the correction.
  3. Too high? Robot overshoots. Too low? Robot reacts slowly.
2. Integral (I):
  1. Accumulates the sum of errors over time.
  2. Helps correct small, steady biases (e.g., unequal motors).
  3. Too high? Causes slow oscillations.
3. Derivative (D):
  1. Measures the rate of change of error.
  2. Predicts future behavior and dampens oscillations.
  3. Too high? Robot may react to sensor noise.
Formula Used:
c
CopyEdit
correction = (Kp * error + Ki * integral + Kd * derivative) / 100;
- Kp, Ki, and Kd are constants chosen based on the behavior of the robot on track.
- Final motor speeds are calculated by adjusting the baseSpeed with the correction.

PID Tuning Procedure (Practical Steps)
1. Start with Ki = 0 and Kd = 0. Set a reasonable baseSpeed (e.g., 80).
2. Increase Kp gradually until the robot begins to follow the line with slight overshooting.
3. Introduce Kd to reduce the overshooting and make the movement smoother, especially around corners.
4. Add a small Ki to correct small drifting or imbalance over time.
5. Test under all conditions — straight paths, tight turns, and cross junctions.
6. Adjust parameters iteratively for optimal behavior.
Example values after tuning:
- Kp = 40
- Ki = 3
- Kd = 25

Optional Enhancements
- Add Bluetooth control for manual override.
- Display real-time PID data on OLED or via Serial Monitor.
- Log sensor readings to SD card for performance analysis.